FENTON PROCESS FOR REMOVING ORGANIC POLLUTANTS FROM INDUSTRIAL WASTEWATER

Dr K. Srilatha*1, B. Mallesham1

1.  ACE College of Engineering, Ankushapur, Ghatkesar, Medchal (Dist), Hyderabad, Telangana, India-501301, Email: drksrilatha@aceec.ac.in , baldhabms@gmail.com.

Abstract:

The fenton process is one of the most studied advanced oxidation processes, due to its efficiency, low reaction time and easy application. In the present study, fenton process is used to remove the organic pollutants from industrial wastewater. The process parameters like pH and reaction time were studied using 1:10 ratio of FeSO4 and H2O2 with a 500ml working volume of sample. The optimum conditions were found at pH 7 with a reaction time of 180 min. Finally, chemical oxygen demands (COD) and chlorides, before and after fenton process were measured to ensure the entire destruction of organics during their removal from industrial wastewater. The experimental results shown that the fenton process effectively achieved removal efficiency of 80%.

Keywords: Industry wastewater, Fenton process, Chemical oxygen demand (COD), chlorides.

1.0 Introduction

In modern years, there has been a crucial necessity to build up effective technologies to remove an increasing number of persistent pollutants, especially from water and wastewater. The natural environment, particularly aquatic ecosystems, is especially sensitive to anthropogenic changes. The development of industry, agriculture, and the development of civilisation and the increase in consumption contribute to the spread and increase in concentrations of a wide range of anthropogenic pollutants in the environment [Popenda et.al., 2018; Kudlek and Dudziak, 2018; Pochwat, 2022]. In recent years, special attention has been paid to the research and implementation of advanced oxidation processes. The common feature of these methods is that they enable the generation of highly reactive hydroxyl (⋅OH) radicals, which react with almost all organic compounds. Owing to the high effciency in the degradation of most organic micropollutants, advanced oxidation methods are now increasingly considered as the most promising alternative treatment methods compared to conventional methods. The Fenton process is an advanced oxidation method [Sabina Ziembowicz et.al. 2022]. Presently, treatment of highly toxic organics present in wastewaters attracts more attention due to their harmful effects to the environment. During the last decades, Fenton’s process has been studied to optimize its efficiency in the depuration of liquid effluents [M Pera-Titus et al., 2004; P Bautista et al., 2008]. This Advanced Oxidation Process (AOP) able to react and remove the organic matter by generating the strong oxidant hydroxyl from the decomposition of hydrogen peroxide in the presence of iron ions at acidic conditions, [M Kitis et al., 1993]. Additionally, the catalytic decomposition of hydrogen peroxide follows a radical mechanism involving hydroperoxyl radicals. Radical chain oxidations will be then initiated by the hydroxyl radicals that will react non-selectively with the organic matter present in the wastewater [E Neyens et al., 2003]. The main advantage of this method is related with the fact that the reaction took place at room conditions of pressure and temperature which makes the treatment less expensive. Moreover, short reaction times are necessary, thus it required easy-to-use reagents [A Guedes et al., 2003]. The Fenton’s process has an important role [F Rivas et al., 2001; A Vlyssides et al., 2004], either to promote the wastewater treatment to accomplish the parameters standard to a safe discharge into the natural water courses, or to minimize the effluent toxicity and enhance its biodegradability to allow an efficient post-biological depuration in municipal wastewater treatment plants. The wastewater toxicity and biodegradability were also measured to predict the possibility of using this chemical oxidation as a pre-treatment to obtain an effluent suitable to be further biologically depurated [I A Balcioglu et.al., 2003; U E Cokgor et.al., 2004; E Neyens et.al., 2003; C M Miller et.al., 1996; W Z Tang et.al., 1997, Pochwat, et.al., 2022].

The presence of many organic contaminants in wastewater results from industrial wastewater and leakage from hazardous compounds storage. The presence of these organic compounds in water poses serious threat to public health since most of them are toxic. For this reason, their removal from the contaminated water is very important. The treatment methods such as biological processes are not effective due to the recalcitrant nature of the contaminants present. Therefore, oxidation processes are preferred to degrade such organics present.

Fenton oxidation was studied extensively by many researchers for the treatment of wastewater containing organic compounds [C M Miller et.al., 1996; W Z Tang et.al., 1997]. Treatment of pharmaceutical wastewater has always been troublesome to reach the desired effluent standards due to the wide variety of the products produced in a drug manufacturing plant, thus fluctuations simultaneously of pollutant concentration will occur. The substances synthesized in a pharmaceutical industry are structurally complex organic chemical that are resistant to biological degradation [I A Balcioglu et.al., 2003]. Due to that, conventional treatment methods are usually inappropriate for the treatment of pharmaceutical wastewaters and hence there is a need for advanced oxidation methods [U E Cokgor et.al., 2004]. Fenton’s oxidation, an advanced oxidation method, appeared to be the most promising method, in terms of cost-effectiveness and ease of operation. Recently, in a comprehensive review, Neyens and Baeyens [E Neyens et.al., 2003] indicated that Fenton’s oxidation is very effective method in the removal of many hazardous organic pollutants from wastewaters. Fenton’s oxidation can also be an effective pre-treatment step by transforming constituents to by-products that are more readily biodegradable and reducing overall toxicity to microorganisms in the downstream biological treatment processes [P Bautista et.al., 2008]. Fenton’s oxidation is one of the best-known metal catalyzed oxidation reactions of water-miscible organic compounds. The Fenton’s reagent has not only oxidation function but also coagulation by the formation of ferric-hydroxo complexes [E Neyens et.al., 2003; A Guedes et.al., 2003]. In the recent past, Fenton reaction was efficiently utilized in wastewater treatment process for the removal of many hazardous organics from wastewater [Nora San et.al., 2003; Nese Ertugay et.al., 2013]. The traditionally accepted Fenton mechanism is represented by following equations [A R Dincer et.al., 2008].

Eqn (1) is recognized as Fenton reaction and implies the oxidation of ferrous to ferric ions to decompose H2O2 into hydroxyl radicals. It is usually considered as the core of the Fenton chemistry:

Fe2+ +H2O2 →Fe3+ + OH- + .OH, K = 40 – 80 L/mols      Eqn (1)

The generated ferric ions can be reduced by reaction with excess hydrogen peroxide to form again ferrous ion and more radicals as shown in Eqn (2).

Fe3+ +H2O2 →Fe2+ + .O2H + H+, K = 9.1 x 10-7 L/mols     Eqn(2)

This reaction is called Fenton-like reaction and slower than Fenton reaction and allows Fe2+ regeneration in an effective cyclic mechanism. In Fenton like reaction, apart from ferrous ion regeneration, hydroperoxyl radicals (HO2-) are produced. The hydroperoxyl radicals may also attack organic contaminants, but they are less sensitive than hydroxyl radicals. It should be noted that, the iron added in small amount acts as a catalyst while H2O2 is continuously consumed to produce hydroxyl radicals.

The following reactions are involved in Fenton chemistry.

Fe2+ + .OH →Fe3+ + OH- , K = 2.5-5 x 108 L/mols Eqn(3)

Fe2+ + .O2H →Fe3+ + HO2- , K = 0.72 – 1.5 x 106 L/mols  Eqn(4)

Fe3+ + .O2H →Fe2+ + O2 + H+, K = 0.33 – 2.1 x 106 L/mols Eqn(5)

Fenton process is encompassing hydrogen peroxide (H2O2) with iron ion’s reaction to form active oxygen species that oxidize organic or inorganic compounds [Huseyin Tekin et.al., 2006].

In recent years, some typical reviews [Ipek Gulkay et.al., 2006; E. Brillas et.al., 2009; R. Chand et.al., 2009; G.M.S. Elshafei  et.al.,  2014; C.K. Wang et.al.,  2015; R. Carta et.al., 2013; X.J. Yang  et.al., 2014; C. Zhang  et.al., 2015; D. Wang et.al., 2014; M. Cat et.al., 2015; Z.P. Wang et.al., 2015; Y. Yang et al., 2009; P. Yan et al., 2014; L. Yu et al., 2014; P. Bautista et al., 2008; G. Pliego et al., 2014] have been published regarding different aspects of the introduction of Fenton/Fenton-like processes. Pliego et al. [G. Pliego et al., 2015], in their review, presented various methods that can enhance Fenton-like processes, such as radiation, electrochemistry, and heterogeneous catalysts; Bautista et al. 2008, provided detailed information on the application of the Fenton process for the treatment of industrial WW. Brillas et.al., 2006 gave a profound introduction to the electro-Fenton processes and the related electrochemical technologies. In our review, the important effect parameters (pH, H2O2 dosage, catalyst dosage, temperature, etc.) are discussed in detail, and then the physical fields/phenomenon-assisted Fenton-like processes are presented.

Fenton-like processes consist of heterogeneous and homogeneous Fenton-like processes. Heterogeneous Fenton-like processes can be established by replacing Fe2+ in the Fenton reagent with a solid catalyst, while homogeneous Fenton-like processes are due to a combination of other metal ion(s)/metal ion-organic ligand complexes and H2O2 [G. Pliego et al., 2015]. In Fenton-like systems pH, H2O2 dosage, catalyst dosage and reaction temperature have been studied widely because of their significant effect on the oxidation capacity of the Fenton-like reagent. Thus, the systematic introduction and analysis of these parameters is necessary.

In the present study, fenton process is used for treating industrial wastewater. The process parameters like pH and reaction time were studied using 1:10 ratio of FeSO4 and H2O2 with a 500ml working volume of sample.

2.0 Materials and Methodology

2.1 Wastewater Characterization

The industrial wastewater sample was collected from the Isnapur industrial site, Hyderabad, (17.29.43N 78.23.34E) Telangana, India. The physicochemical characterization of wastewater samples was carried using “standard methods for examination of water and wastewater 21st addition-2005, APHA” [Jotin R et al., 2012; Bhagawan D et al., 2017, Sabina et.al., 2022]. The initial characterization of chloro pesticide intermediate industrial wastewater sample was given in Table 1.

Table 1 Initial characterization of chloro pesticide intermediate industrial wastewater sample

| S. No | Parameter | Concentration |
| --- | --- | --- |
| 1 | pH | 1.29 |
| 2 | EC | 103.8ms/cm |
| 3 | COD | 90,000mg/l |
| 4 | Chlorides | 34,450mg/l |
| 5 | Total Solids (TS) | 75,500mg/l |
| 6 | Total Dissolved Solids (TDS) | 55,000mg/l |
| 7 | Suspended Solids (SS) | 20,500mg/l |
| 8 | Sulphates | 1,685mg/l |
| 9 | Total Organic Carbon (TOC) | 42,390mg/l |

2.2 Fenton Process for treating chloro pesticide intermediate industrial wastewater

According to theoretical calculations, the required quantity of hydrogen peroxide and iron sulphate (1:10 ratio) were added to 300ml working volume of sample and kept it in a shaker under closed conditions. The samples were collected for every 1hr till 3hrs of reaction time and then again kept it in a shaker for 24hrs to check the degradability of the sample. The samples were filtered with Whatmann filter paper and analyzed using standard methods (APHA 2005) [Ashok KC et al., 2013, Pochwat, 2022 & Sabina 2022].

2.3 Removal Percentage Calculation

The quantitative reduction of pollutants was measured according to the APHA standard methods [APHA 2005] and the percentage removal was calculated using Eqn-6.

% Removal = (C0 - Ct) × 100/Ct                               Eqn (6)

Where, C0 = Initial Concentration, Ct = Final Concentration

3.0 Results and Discussions

3.1 Initial physicochemical characterization of chloro pesticide intermediate industrial wastewater

The initial physicochemical characterization of chloro pesticide intermediate industrial wastewater sample was performed and shown in Table 2.

Table 2 Initial physicochemical characteristics of chloro pesticide intermediate industrial wastewater sample

| S. No | Parameter | Initial Concentration | Central Pollution Control Board (CPCB) Limits |
| --- | --- | --- | --- |
| 1 | pH | <2 | 6.0-9.0 |
| 2 | Electrical Conductivity [EC] | 103.8ms/cm | NA |
| 3 | Chemical Oxygen Demand | 90,000mg/l | 250mg/l |
| 4 | Sulphates | 1,685mg/l | 400mg/l |
| 7 | Total Solids [TS] | 75,500mg/l | NA |
| 8 | Total Dissolved Solids [TDS] | 55,000mg/l | NA |
| 9 | Chlorides | 34,450mg/l | NA |
| 10 | Total Organic Carbon [TOC] | 42,390mg/l | NA |

Note: All the parameters were expressed in mg/l, except pH, EC. EC expressed in Milli Siemens and NA-Not Applicable.

3.2 Effect of Fenton process for the treatment of chloro-pesticide intermediate industrial wastewater

3.2.1 Effect of reaction time and pH

Effect of reaction time is one of the effecting parameters in treatment of chloro pesticide intermediate industrial wastewater using fenton process. The effect of reaction time (30, 60, 90, 120, 150, 180Min & 24hr) studied at different pHs (<2, 3 & 7) and which were shown in the following figures. The maximum removal has been observed at reaction time of 3hr. This might be due to sufficient dosage and after 3hr of reaction time, it maintained constant. Hence, to avoid excess operational cost the reaction time is optimized to 3hr of reaction time.

Fig.1 Removal Percentage of Chlorides at pH <2

Fig.2 Removal Percentage of Chlorides at pH 3

Fig.3 Removal Percentage of Chlorides at pH 7

Fig.4 Removal Percentage of COD at pH <2

Fig.5 Removal Percentage of COD at pH 3

Fig.6 Removal Percentage of COD at pH 7

From Fig 1, 2, 3, 4, 5 and 6, we observed that the removal percentage of COD and chlorides increased with increasing the pH and reaction time. The maximum removal achieved at pH 7. At this pH, the removal % of COD and chlorides are 80 and 78% respectively at 180Min of reaction time.

The pH value has a decisive effect on the oxidation potential of OH. radicals due to its reciprocal relation of the oxidation potential to the pH value. Furthermore, the concentration of inorganic carbon and the hydrolytic speciation of Fe (III) species are strongly affected by the pH value. Therefore, the role of pH in the Fenton reaction must be determined. The same as in Fenton and Fenton-like reactions have a maximum catalytic activity at pH of about 2.8–3. The pH value influences the generation of OH. radicals and thus the oxidation efficiency. For pH values above 6, the degradation strongly decreases since iron precipitates as hydroxide derivate, reducing the Fe (II) availability and the radiation transmission. Another reason for the inefficient removal at pH > 3 is due to the dissociation and auto-decomposition of H2O2.

3.2.2 The removal percentage of chlorides

The removal percentage of chlorides at pH 1.29, 3 and 7 were given in following figures 7, 8 & 9. With increasing the reaction time, removal percentage of Chlorides also increased.

Fig.7 Removal Percentage of Chlorides at pH 1.29

Fig.8 Removal Percentage of Chlorides at pH 3

Fig.9 Removal Percentage of Chlorides at pH 7

4.0 Conclusions

The Fenton process is advanced process which is used to remove the contaminants from water and wastewater, and it has wide application on an industrial scale. The maximum removal percentage of chlorides and COD obtained with fenton process at pH 7.

References

A Guedes, L Madeira, R Boaventura, C Costa (2003) Fenton oxidation of cork cooking wastewater–overall kinetic analysis. Water Res. 37: 3061–3069.

A R Dincer, N Karakaya, E Gunes, Y Gunes (2008) Removal of COD from oil recovery industry wastewater by the Advanced Oxidation Processes (AOP) based on H2O2. Global NEST Journal 10: 31-38.

A Vlyssides, H Loukakis, P Karlis, E Barampouti, S Mai (2004) Olive mill wastewater detoxification by applying pH related Fenton’s oxidation. Fresenius Environ. Bull. 13: 501–504.

Ashok KC, Sharma AK (2013) Removal of turbidity. COD and BOD from secondarily treated sewage water by electrolytic treatment. Appl Water Sci. doi:10.1007/s13201-012-0066-x.

B G Kwon, D S Lee, N Kang, J Yoon (1999) Characteristics of pchlorophenol oxidation by Fenton’s reagent. Water Res. 33: 2110–2118.

Bhagawan D, Saritha Poodari, Chaitanya narala, Ravi surya, Yamuna Rani. M, Vurimindi Himabindu, S Vidyavathi (2017) Industrial solid waste landfill leachate treatment using Electrocoagulation and Biological methods, Desalination and Water Treatment, 68: 137–142. doi:10.5004/dwt.2017.20335.

C M Miller, R L Valentine, M E Roehl, P J J Alvarez (1996) Chemical and microbiological assessment of pendimethalin-contaminated soil after treatment with Fenton’s reagent. Water Res. 30: 2579– 2586.

C. Zhang, M.H. Zhou, G.B. Ren, X.M. Yu, L. Ma, J. Yang, F.K. Yu, Heterogeneous electro-Fenton using modifiedironecarbon as catalyst for 2,4-dichlorophenol degradation: influence factors, mechanism and degradation pathway, Water Res. 70 (2015) 414–424.

C.K. Wang, Y.H. Shih, Degradation and detoxification of diazinon by sono-Fenton and sono-Fenton-like processes, Sep. Purif. Technol. 140 (2015) 6–12. A.Y. Atta, B.Y. Jibril, T.K. Al-Waheibi, Y.M. Al-Waheibi, Microwave-enhanced catalytic degradation of 2-nitrophenol on alumina-supported copper oxides, Catal. Commun. 26 (2012) 112–116.

C.W. Yang, D. Wang, Q. Tang, The synthesis of NdFeB magnetic activated carbon and its application in degradation of azo dye methyl orange by Fenton-like process, J. Taiwan Inst. Chem. Eng. 45 (2014) 2584–2589.

Ctia Oliveira, Arminda Alves, Luis M Madeira (2014) Treatment of water networks (waters and deposits) contaminated with chlorfenvinphos by oxidation with Fenton’s reagent. Chemical Engineering Journal 241: 190–199

E G Solozhenko, N M Soboleva, V V Goncharuk (1995) Decolorization of azo dye solutions by Fenton’s oxidation. Water Res. 29: 2206–2210.

E Neyens, J Baeyens (2003) A review of classic Fenton’s peroxidation as an advanced oxidation technique. J. Hazard. Mater. 98: 33–50.

E Neyens, J Baeyens (2003) A review of classic Fenton’s peroxidation as an advanced oxidation technique, J. Hazard. Mater. 98: 33– 50.

E. Brillas, I. Sires, M.A. Oturan, Electro-Fenton process and related electrochemical technologies based on Fenton’s reaction chemistry, Chem. Rev. 109 (2009) 6570–6631.

F Rivas, F Beltrin, O Gimeno, J Frades (2001) Treatment of olive mill wastewater by Fenton’s reagent. J. Agric. Food Chem. 49: 1873–1880.

G. Pliego, J.A. Zazo, P. Garcia-Munoz, M. Munoz, J.A. Casas, J.J. Rodriguez, Trends in the intensification of the Fenton process for wastewater treatment- An overview, Crit. Rev. Env. Sci. Technol. 45 (2015) 2611–26.

G.M.S. Elshafei, F.Z. Yehia, O.I.H. Dimitry, A.M. Badawi, G. Eshaq, Ultrasonic assisted-Fenton-like degradation of nitrobenzene at neutral pH using nanosized oxides of Fe and Cu, Ultrason. Sonochem. 21 (2014) 1358–1365.

Huseyin Tekin, Okan Bilkay, Selale S. Ataberk, Tolga H Balta, I Haluk Ceribasi, et al. (2006) Use of Fenton oxidation to improve the biodegradability of a pharmaceutical wastewater, Journal of Hazardous Materials B 136: 258–265.

I A Balcioglu, M Otker (2003) Treatment of pharmaceutical wastewater containing antibiotics by O3 and O3/H2O2 processes. Chemosphere 50: 85–95.

I Casero, D Sicilia, S Rubio, D Perez-Bendito (1997) Chemical degradation of aromatic amines by Fenton’s reagent. Water Res. 31: 1985–1995.

Ipek Gulkay, Gulerman A Surucu, Filiz B Dilek (2006) Importance of H2O2/Fe2+ ratio in Fenton’s treatment of a carpet dyeing wastewater. Journal of Hazardous Materials B136: 763–769.

J L Morais, P P Zamora (2005) Use of advanced oxidation processes to improve the biodegradability of mature landfill leachates. J. Hazard. Mater. 123: 181–186.

Jotin R, Ibrahim S, (2012) Halimoon, Electro coagulation for removal of chemical oxygen demand in sanitary landfill leachate. Int. J. Environ. Sciences 3: 921-930.2.

Kudlek, E., Dudziak, M., 2018. Degradation pathways of pentachlorophenol and benzo
(a)pyrene during heterogeneous photocatalysis. Water Sci. Technol. 77 (10),
2407–2414. https://doi.org/10.2166/wst.2018.192.

L. Yu, C.P. Wang, X.H. Ren, H.W. Sun, Catalytic oxidative degradation of bisphenol A using an ultrasonic-assisted tourmaline-based system: influence factors and mechanism study, Chem. Eng. J. 252 (2014) 346–354.

Libing Chu, Jianlong Wanga, Jing Dong, Haiyang Liu, Xulin Sun (2012) Treatment of coking wastewater by an advanced Fenton oxidation process using iron powder and hydrogen peroxide. An international Chemosphere journal 86: 409–414.

M Kitis, C Adams, G Daigger (1999) The effects of Fenton’s reagent pre-treatment on the biodegradability of non-ionic surfactants. Water Res. 33: 2561–2568.

M Pera-Titus, V Garcia-Molina, M Banos, J Gimenez, S Esplugas (2004) Degradation of chlorophenols by means of advanced oxidation processes: a general review. Appl. Catal. B 47: 219–256.

M. Catala, N. Dominguez-Morueco, A. Migens, R. Molina, F. Martinez, Y. Valcarcel, N. Mastroianni, M. Lopez de Alda, D. Barcelo, Y. Segura, Elimination of drugs of abuse and their toxicity from natural waters by photo-Fenton treatment, Sci. Total Environ. 520 (2015) 198–205.

Nese Ertugay, Filiz Nuran Acar (2013) Removal of COD and color from Direct Blue 71 azo dye wastewater by Fenton’s oxidation: Kinetic study. Arabian Journal of Chemistry.

Nora San Sebastián Mart´ınez, Josep F´ıguls Fernández, Xavier Font Segura, Antoni Sánchez Ferrer Escola (2003) Pre-oxidation of an extremely polluted industrial wastewater by the Fenton’s reagent. Journal of Hazardous Materials B 101: 315–322.

P Bautista, A Mohedano, J Casas, J Zazo, J Rodriguez (2008) An overview of the application of Fenton oxidation to industrial wastewaters treatment. J. Chem. Technol. Biotechnol. 83: 1323–1338.

P. Bautista, A.F. Mohedano, J.A. Casas, J.A. Zazo, J.J. Rodriguez, An overview of the application of Fenton oxidation to industrial wastewaters treatment, J. Chem. Technol. Biotechnol. 83 (2008) 1323–1338.

Pochwat, K., 2022. Assessment of rainwater retention effciency in urban drainage systems—model studies. Resources 11 (2), 14. https://doi.org/10.3390/ resources11020014.

Popenda, A., Włodarczyk-Makuła, M., 2018. Hazard from sediments contaminated with
persistent organic pollutants (POPs). Desalination Water Treat. 117, 318–328.
https://doi.org/10.5004/dwt.2018.22529.

P. Yan, L.B. Gao, W.T. Li, Microwave-enhanced Fenton-like system Fe3O4/H2O2, for Rhodamine B wastewater degradation, Appl. Mech. Mater. 448–453 (2014) 834–837.

R. Carta, F. Desogus, The enhancing effect of low power microwaves on phenol oxidation by the Fenton process, J. Environ. Chem. Eng. 1 (2013) 1292–1300.

R. Chand, N.H. Ince, D.H. Bremner, Phenol degradation using 20, 300 and 520 kHz ultrasonic reactors with hydrogen peroxide or ozone and zero valent metals, Sep. Purif. Technol. 67 (2009) 103–109.

Sabina Ziembowicz, Malgorzata Kida (2022) Limitations and future directions of application of the Fenton-like process in micropollutants degradation in water and wastewater treatment: A critical review. Chemosphere 296 (2022) 134041.

S F Kang, H M Chang (1997) Coagulation of textile secondary effluents with Fenton’s reagent. Water Sci.Technol. 36: 215–222.

S Karthikeyan, A Titus, A Gnanamani, A B Mandal, G Sekaran (2011) Treatment of textile wastewater by homogeneous and heterogeneous Fenton oxidation processes. Desalination journal: 438–445.

Soraya Mohajeri, Hamidi Abdul Aziz, Mohamed Hasnain Isa, Mohammed J K Bashir, Leila Mohajeri, et al. (2010) Influence of Fenton reagent oxidation on mineralization and decolorization of municipal landfill leachate. Journal of Environmental Science and Health Part A 45: 692–698.

U E Cokgor, I A Alaton, O Karahan, S Dogruel, D Orhon (2004) Biological treatability of raw and ozonated penicillin formulation effluent. J. Hazard. Mater. 116: 159–166.

V Kavitha, K Palanivelu (2005) Destruction of cresols by Fenton oxidation process. Water Res. 39: 3062–3072.

W G Kuo (1992) Decolorizing dye wastewater with Fenton’s reagent. Water Res. 26: 881–886.

W Z Tang, C P Huang (1996) An oxidation kinetic model of unsaturated chlorinated aliphatic compounds by Fenton’s reagent. J. Environ. Sci. Health A 31: 2755–2775.

W Z Tang, S Tassos (1997) Oxidation kinetics and mechanisms of trihalomethanes by Fenton’s reagent. Water Res. 31: 1117– 1125.

X.J. Yang, P.F. Tian, X.M. Zhang, X. Yu, T. Wu, J. Xu, Y.F. Han, The generation of hydroxyl radicals by hydrogen peroxide decomposition on FeOCl/SBA- 15 catalysts for phenol degradation, AlChE J. 61 (2014) 166–176.

Y. Yang, P. Wang, S. Shi, Y. Liu, Microwave enhanced Fenton-like process for the treatment of high concentration pharmaceutical wastewater, J. Hazard. Mater. 168 (2009) 238–245.

Z.P. Wang, Y.Z. Guo, Z.Z. Liu, X.N. Feng, Y.Q. Chen, T. Tao, Catechin as a new improving agent for a photo-Fenton-like system at near-neutral pH for the removal of Inderal, Photochem. Photobiol. Sci. 14 (2015) 473–480.